Carnegie Mellon University
Department of Civil and Environmental Engineering

12-725: Fate and Transport of Organic Compounds in Aquatic Systems
Exam 2 (4/9/20)
(107 Points Total)

1. 1,2,3-trichloropropane (1,2,3-TCP) was used as a cleaning and degreasing agent. It is a known carcinogen, and agencies are required to report its detection in water samples if it is detected at 5 parts-per-trillion or higher.

Even though 1,2,3-TCP has been used for some time, the fate and transport of 1,2,3-TCP has not been evaluated extensively. The following information is available about 1,2,3-TCP.

Molecular Weight:	147
Density:	1.3 g/cm3
Melting Point:	-14 ºC
Log Kow	2.5
Boiling Point:	158 ºC
Di,w (25 °C)	7.9 x 10-10 m2/s
Vapor Pressure	5x10-3 atm
Water Solubility	10 mM
Enthalpy of vaporization	38 kJ/mol

1.	(40 points total) You are an environmental engineer working on a remediation project for a site contaminated by 1,2,3-TCP. You are asked to evaluate the feasibility of using a soil vapor extraction (SVE) system to remove 1,2,3-TCP present in an unsaturated aquifer. A soil vapor extraction unit applies vacuum to an unsaturated aquifer and removes contamination that is present in the vapor phase that is being removed from the unsaturated pore spaces.

(a) (20 pts) Determine the fraction of mass of 1,2,3-TCP in each of the compartments of a partially saturated soil (i.e. soil, water, air) assuming enough time has elapsed such that equilibrium is obtained. Assume the soil has a total porosity of 0.45 and maintain 60% water saturation (i.e. 60% of the pore space is water filled and 40% of the pore space is air filled). Assume that the soil particle density, s, is 2.5 g cm-3, and the fraction organic carbon is 1.0%.
(b)	(10 pts) If this aquifer were in a coastal region such that the water in the pore space were more like seawater rather than groundwater, how would this affect your answer to part (a)? NOTE: You do not need a quantitative answer, only a qualitative description, i.e. direction of the change and the rationale for your answer.
(c) (10 pts) Using the result from part (a), and assuming that the SVE unit can remove 20 pore volume of air per day and that the local equilibrium assumption is valid, estimate the number of days required to remove 99.5% of the 1,2,3-TCP mass present in the aquifer. Is SVE a viable option for treatment under these conditions? Why or why not?
2.	(25 points total) You own a manufacturing facility that uses two solvents during manufacture of different products. You have contaminated process water in a holding tank with the following compounds and concentrations.

Compound	Concentration (mg/L)	MW (g/mol)
Toluene	22	92.1
Phenol	4	94.1

(15 pts) For the specific mixing conditions in the tank, the following mass transfer coefficients were measured for CO2 and water, respectively.

vCO2,w=4.6e-2 cm/s, VH2O,g=1.1 cm/s

What is the overall mass transfer coefficient for each compound in the system?

(b)	(5 points) If the tank has a total volume of 60 m3 and a surface area of 8 m2, what is the half life time of each compound in the tank, assuming no losses other than volatilization?

(c)	(5 points) Why do these two very similarly sized compounds behave differently?

3. (12 points) This figure below shows the relationship between KiDOC and Kiow for three classes of ompounds. Explain why PAHs and alkanes may have different KiDOC values for the same Kiow.

4. (30 points) Clay layers are often used as landfill liners to contain chemicals that have accidently been put into the landfill. If you define the breakthrough of a chemical as the time it takes for the concentration at the outside edge of the layer to reach ½ of the chemical’s concentration on the inside edge of the clay layer, would you expect a 1cm thick bentonite clay landfill liner to prevent leakage of benzene (r=0.88g/cm3, MW=78 g/mol) for 30 years? State any assumptions that you make about the system.

Some useful properties of bentonite clay: s=1.8 g/cm3, porosity=0.3, tortuosity, =4.

The following formulas, physical constants, and properties may be useful.

Viscosity of water at 20 C	10-3 kg m-1 s-1
Density of water at 20 C	998 kg m-3
Diffusivity of Carbon Dioxide in water at 20 C	1.67 x 10-9 m2 s-1
Molar mass of air at 20 C	28.96 g/mol
Molar volume of air at 20C	22.4 L/mol
Universal Gas Constant, R	82.06 atm m3 mol-1 K-1 / 0.08206 L atm mol-1 K-1 / 8.314 J mol-1 K-1
Atmospheric pressure	1 atm / 760 torr / 101.3 kPa
Thermodynamic Relationships
Aqueous Concentration relationships	Ci (mol L-1)=xi­­ Vw-1 = xi  55.5 mol L-1
Clayperon Equation
Kistiakowsky’s expression
Prausnitz/Yalkowsky

Chlorinated alkanes, benzenes, and PCBs

Air-water exchange velocity relationships

Sciw=660 at 20 °C.

, where a=1, 0.5, or 2/3 depending on the model assumed
 Or based on mass
, where a=1, 0.5, or 2/3 depending on the model assumed

Diffusivity in air and water